## Slide 1
Validation of pharmaceutical process,
Analytical Method development
Computer system validation, ERP

## Slide 2: LIST OF CONTENTS
Process validation
Introduction
Type of validation
Stage of validation
Major phase of validation
SOP
Validation report

## Slide 3: Method Validation
“Method validation is the process of demonstrating that analytical procedures are suitable for their intended use and that they support the identity, strength, quality, purity and potency of the drug substances and drug products.
Method validation is continuous process. The goal is to insure confidence in the analytical data throughout product development.

## Slide 4: Essentials of Pharmaceutical Validation
Validation is an integral part of quality assurance; it involves the systematic study of systems, facilities and processes aimed at determining whether they perform their intended functions adequately and consistently as specified
A validated process is one which has been demonstrated to provide a high degree of assurance that uniform batches will be produced that meet the required specifications and has therefore been formally approved.

## Slide 5
Type of validation
Prospective validation
  pre-planned protocol
  It makes an integral part of a carefully planned, logical product /process developmental program. (Figure 1)
Concurrent validation
  base on data collected during actual performance of a process already implemented in a manufacturing facility
  suit manufacturers of long standing, have well-controlled manufacturing process
Retrospective validation
  for production for a long time, but has not been validated according to a prospective protocol and concurrent validation is not realistic option (is not generally accepted)

## Slide 7
Adequate validation is beneficial to the manufacturer in many ways:
It deepens the understanding of processes; decreases the risk of preventing problems and thus assures the smooth running of the process.
It decreases the risk of defect costs.
It decreases the risk of regulatory noncompliance.
A fully validated process may require less in-process controls and end product testing.
Validation should thus be considered in the following situations:
Totally new process;
New equipment;
Process and equipment which have been altered to suit changing priorities; and
Process where the end-product test is poor and an unreliable indicator of product quality.

## Slide 8: The validation steps recommended in GMP guidelines can be summarized as follows
all studies should be conducted in accordance with a detailed, pre-established protocol or series of protocols, which in turn is subject to formal – change control procedures;
All data generated during the course of studies should be formally reviewed and certified as evaluated against pre-determined criteria;
Suitable testing facilities, equipment, instruments and methodology should be available;
The personnel should be trained and qualified and be suitable and competent to perform the task assigned to them;
Comprehensive documentation should be available to define support and record the overall validation process.
Suitable clean room facilities should be available in both the ‘local’ and background environment.

## Slide 9: Strategy for Methods Validation
The validity of a specific method should be demonstrated in laboratory experiments using samples or standards that are similar to the unknown samples analyzed in the routine.
Develop a validation protocol or operating procedure for the validation;
Define the application purpose and scope of the method;
Define the performance parameters and acceptance criteria;
Define validation experiments;
Verify relevant performance characteristics of the equipment;
Select quality materials, e.g., standards and reagents;
Perform pre-validation experiments;
Adjust method parameters and/or acceptance criteria, if necessary;
Perform full internal (and external) validation experiments;
Develop SOPs for executing the method routinely;
Define criteria for revalidation;

## Slide 10
Validation has to be planned and carried out in an organized
manner. Typical steps often consist of
1. Validation Specification Development
Design Specification
Functional Specification
User Requirement Specification
2. Validation Protocols
3. Validation Phases (GAMP V)
DQ- Design Qualification
IQ- Installation Qualification
OQ-Operational Qualification
PQ- Performance Qualification

## Slide 11
Design qualification (DQ)
  necessary when planning and choosing EQ or systems to ensure that components selected will have adequate capacity to function for the intended purpose, and will adequately serve the operations or functions of another piece of EQ or operation.
Installation Qualification (IQ)
all major processing and packaging equipment, and ancillary systems are in conformity with installation specification, equipment manuals schematics and engineering drawing.

## Slide 12
Operational Qualification (OQ)
  should provide a listing of SOPs for operation, maintenance and calibration
  define the specification and acceptance criteria
  include information on EQ or system calibration, pre-operational activities, routine operations and their acceptance criteria
Performance Qualification (PQ)
  This verifies that the system is repeatable and is consistently producing a quality product.
  performed after both IQ and OQ have been completed, reviewed and approved
  include description of preliminary procedures required, detailed performance tests to be done, acceptance criteria

## Slide 13: Major Phases in PROCESS Validation
The activities relating to validation studies may be classified into three:
Phase 1: (Pre-validation Qualification Phase)
which covers all activities relating to product research and development, formulation pilot batch studies, scale-up studies, transfer of technology to commercial scale batches, establishing stability conditions and storage, and handling of in-process and finished dosage forms, equipment qualification, installation qualification, master production document, operational qualification and process capacity.

## Slide 14
Phase 2: This is the Process Validation Phase. It is designed to verify that all established limits of the critical process parameter are valid and that satisfactory products can be produced even under the worst conditions.
Phase 3: Known as the Validation Maintenance Phase, it requires frequent review of all process related documents, including validation of audit reports, to assure that there have been no changes, deviations, failures and modifications to the production process and that all standard operating procedures (SOPs), including change control procedures, have been followed.

## Slide 15
Process validation
specific process clearly described in Master formula or in SOP
  all EQ; identity, code number, construction, operation capacity, actual operating range
  processing parameter; sufficiently detailed to permit complete reproducibility (time period, pH, volume, temp.etc.)
  specification at each step
Very important
  specifications for a process undergoing validation be pre-determined
  all critical processing parameters for which specifications have been set, there must be equipment to measure all of those parameters during the validation study

## Slide 16
~ Standard Operating Procedures (SOPs) ~
System SOPs
  Procedures that describe how to use the system
  May reference User Guides
Operational SOPs
  Should incorporate the automation being introduced by the system that will replace manual process.
Computer System Validation SOPs
  Document Management
  Security (Logical and Physical)
  Training
  Backup and Restore
  System testing (Validation and Verification)
  Change Control and Configuration Management
  Problem Resolution
  Periodic Review and Monitoring
  Disaster Recovery

## Slide 17
The Validation Report
A written report should be available after completion of the validation. If found acceptable, it should be approved and authorized (signed and dated). The report should include at least the following:
Title and objective of study;
Reference to protocol;
Details of material;
Equipment;
Programmes and cycles used;
Details of procedures and test methods;
Results (compared with acceptance criteria); and
Recommendations on the limit and criteria to be applied on future basis.

## Slide 18
Validation: changes that require revalidation
Software changes; controllers
Site changes; operational changes
Change of source of material
Change in the process
Significant equipment changes
Production area changes
Support system changes

## Slide 19
Analytical Method development
Specifications for materials and products, with standard test methods
Manufacturer to use “pharmacopoeial specifications and methods”, or suitably developed “non-pharmacopoeial specifications and methods” approved by national regulatory agencies.
Use well-characterized reference materials, with documented purity, in the validation study
Tests include:
  identification tests
  assay of drug substances and pharmaceutical products
  content of impurities and limit tests for impurities
  dissolution testing and determination of particle size
Results should be reliable, accurate and reproducible

## Slide 20: Quality element required for method development & validation
Quality element | Description
Quality assurance unit | Resposible for the duties related to QA
Adequate laboratory facilities | Facilities with adequate space, appropriate environmental conditions , security, & control system, including analytical instrumentation & equipment
Quality personnel | Suitable employees with suitable education ,training & experience to laboratory working
Training program | Provides effective regulatory, safety, procedural & profeciency training
Written procedures | Such as SOP, testing procedures
Document control | Data handling & management, report generation, record retention & retrieval
Change control | Chronicles changes made to all of the quality elements
Internal audits | Demonstrate compliance & all effectiveness to all of the quality elements

## Slide 21: Considerations Prior To Method Validation
Suitability of Instrument
  Status of Qualification and Calibration
Suitability of Materials
  Status of Reference Standards, Reagents, etc.
Suitability of Analyst
  Status of Training and Qualification Records
Suitability of Documentation
  Written analytical procedure and proper approved protocol with pre-established acceptance criteria.

## Slide 22
[Pharmacopoeial/Non-pharmacopoeial methods
Pharmacopoeial methods:
  prove that the methods are suitable for routine use in the laboratory (verification)
  for determination of content or impurities in products, demonstrate that method is specific for the substance under consideration (no placebo interference)
Non-pharmacopoeial methods:
  Should be appropriately validated

## Slide 23: Examples Of Methods That Require Validation Documentation
Chromatographic Methods
Spectrophotometric Methods
Capillary Electrophoresis Methods
Particle Size Analysis Methods
Dissolution Methods
Titration Methods
Automated Analytical Methods

## Slide 24: Regulatory Approaches
Compendial Analytical Procedures
Noncompendial Analytical Procedures and Validation Requirements
1. Compendial Analytical Procedures
The Analytical procedures in the USP 25/NF 20 are legally recognized under section 501(b) of the Federal Food, Drug and Cosmetic Act as the regulatory analytical procedures for the compendial items. The suitability of these procedures must be verified under actual conditions of use.

## Slide 25
When using USP 25/NF 20 analytical procedures, the guidance recommends that information be provided for the following characteristics:
  Specificity of the procedure
  Stability of the sample solution
  Intermediate precision
Compendial analytical procedures may not be stability indicating, and this concern must be addressed when developing a drug product specification because formulation-based interference may not be considered in the monograph specifications.

## Slide 26: 2. Noncompendial Analytical Procedures and Validation Requirements
The most widely applied validation characteristics for noncompendial procedure are accuracy, precision, specificity, detection limit, quantitation limit, linearity, range and robustness.
At the time of NDA and ANDA submission to FDA, the applications should contain the above validation information to support the adequacy of the analytical procedures.

## Slide 27: VALIDATION MASTER PLAN (VMP) FOR ANALYTICAL METHODS
Step 1 : select the validation team & define the roles of each team member
Step 2 : define the techanical & regulatory objectives
Step 7 : review the data Vs acceptance criteria set forth in the validation protocol ( A failure may change the validation protocol , back to step 5, if necessary)
Step 8 : write the final validation report
Step 9 : ongoing evaluation of the method
Step 10 : revalidation of the method
Step 3 : select the analytical technique
Step 4 : develop & document the analytical method
Step 5 : select the validation parameters & prepare a validation protocol
Step 6 : perform & document the validation
Notes: Step 2 :

## Slide 28
METHOD DEVELOPMENT
Defining the technical requirement
Considering the required precision
Considering the required detection limit
Selecting an analytical technique
The analytical method
Using an Exisiting method Modifying or optimizing an Developing a new analytical
Existing method method
Demonstrating method feasibility
Developing system suitability
Documenting the analytical method
Reference Standard Qualification
Qualification of a sourced Qualification of a synthesized reference
Reference standard material Standard material
Method validation
Figure : The validation process from method development to method validation

## Slide 29: Elements of a Protocol
Specificity
Linearity
Accuracy and Range
LOD/LOQ
Precision
Ruggedness
Robustness (Ideally in MD Phase)
System Suitability Testing

## Slide 30
Specificity –
The ability to accurately & reproducible generate results that don’t false positive.
Specificity is the freedom from interference caused by substances other than the intended compounds (impurities, degradants, matrix ).
LINEARITY - of an analytical procedure is its ability (within a given range) to obtain test results which are directly proportional to the concentration (amount) of analyte in the sample.

## Slide 31
DETERMINATION- Linearity should be evaluated by visual inspection of a plot of signals as a function of analyte concentration or content.
Note:- For the establishment of linearity, a minimum of five concentrations is recommended.
RANGE - of an analytical procedure is the interval between the upper and lower concentration (amounts) of analyte in the sample (including these concentrations) for which it has been demonstrated that the analytical procedure has a suitable level of precision, accuracy and linearity.
The specified range is normally derived from linearity studies and depends on the intended application of the procedure.

## Slide 33
ACCURACY - of an analytical method is the closeness of test results obtained by that method to the true value.
This definition incorporate both precision & specificity.
Accuracy is giving the laboratory & clinician the right answer, & describing the conc. Of analyte that actually present.
Note:- Accuracy should be assessed using a minimum of 9 determinations over a minimum of 3 concentration levels covering the specified range.
PRECISION- the reproducibility of replicate analyses at different levels of the analyte , within assay & between assay.
Expression of Precision
Repeatability
Intermediate precision
Reproducibility

## Slide 34
DETECTION LIMIT of an individual analytical procedure is the lowest amount of analyte in a sample which can be detected but not necessarily quantitated, under the stated experimental conditions.
depending on whether the procedure is a non-instrumental or instrumental.
BASED ON VISUAL EXAMINATION
BASED ON SIGNAL TO NOISE RATIO
  standard deviation of the response and the slope
  standard deviation of the blank
  calibration curve

## Slide 35
QUANTITATION LIMIT of an individual analytical procedure is the lowest amount of analyte in a sample which can be quantitatively determined with suitable precision and accuracy.
RUGGEDNESS of an analytical method is the degree of reproducibility of test results obtained by the analysis of the same samples under a variety of conditions, such as different laboratories different analyst, different instruments, different lots of reagent, different elapsed assay times, different assay temperatures, different days, etc.

## Slide 36
ROBUSTNESS - of an analytical procedure is a measure of its capacity to remain unaffected by small, but deliberate variations in method parameters and provides an indication of its reliability during normal usage.
The evaluation of robustness should be considered during the development phase and depends on the type of procedure under study.
SYSTEM SUITABILITY TESTING - is an integral part of many analytical procedures. The tests are based on the concept that the equipment, electronics, analytical operations and samples to be analyzed constitute an integral system that can be evaluated as such.

## Slide 38: PUBLISHED GUIDENCE’S
  ICH-Q2A “Text on Validation of Analytical Procedure:(1994)
  ICH-Q2B “Validation of Analytical Procedures: Methodology: (1995)
  CDER “Reviewer Guidance: Validation of Chromatographic Method” (1994)
  CDER “Submitting Samples and Analytical Data for Method Validations” (1987)
  CDER Draft “Analytical Procedures and Method Validation” (2000)
  CDER “Bioanalytical Method Validation for Human Studies” (1999)
  USP<1225> “Validation of Compendial Methods” (current revision)

## Slide 39: COMPUTER SYSTEM VALIDATION
List of contents -
Introduction
Objective
Guidance documents for computerized systems
History of electronic spread sheet
Validation of computer system
References

## Slide 40: INTRODUCTION
The FDA requires that these computer systems, an integral component of research and development, manufacturing, distribution, sales and marketing, must be properly developed, tested and used according to the formal quality standards.
To establish the evidence and the associated documentation that a system meets these standards and that it will continue to do so over the time, requires Computer System Validation.

## Slide 41: Guidance Documents For Computerized Systems (USFDA)
April 1999 | Computerized Systems Used in Clinical Trials
September 1999 | Off-The-Shelf Software Use in Medical Devices
August 2001 | Electronic Records; Electronic Signatures – Validation
January 2002 | General Principles of Software Validation
August 2003 | Electronic Records; Electronic Signatures - Scope and Application
21 CFR Part 11 | Electronic Records; Electronic Signatures
21 CFR Part 820 | Quality System Regulation

## Slide 42: Harmonization efforts..
Discussion on the integrity of data and computer software validity in section 5.8 of ICH
Government Paper-work elimination Act, title XVII, signed on 21st October 1998, mandates all agencies (including FDA) to accept all documentation and signatures in the electronic form by October 2003
In 2005, HIPAA ( Health Insurance Portability and Accountability Act) electronic security standards became effective.(21 CFR Part 11 are directly applicable to compliance with the new HIPAA regulations)
TGA GMP has acquired electronic audit trials since 1991
ELECTRONIC SPREADSHEET | YEAR OF DEBUT | LAUNCHER
VisiCalc | 1978 | Harvard Business School
Lotus 1-2-3 | 1983 | IBM
Excel | 1984 | Microsoft Corporation

## Slide 43
Objectives
To discuss validation of computerized systems including:
System specifications
Functional specifications
Security
Back-ups
Validation:
  Hardware
  Software
  Production and quality control.

## Slide 44: GENERAL
Computer systems used in planning, specification, programming, testing, commissioning, document operation, monitoring and modifying.
Validation: Evidence and confidence
  intended use, accuracy, consistency and reliability.
  Both the system specifications and functional specifications should be validated.
Periodic (or continuous) evaluation should be performed after the initial validation.
Written procedures for:
  performance monitoring, change control, programme and data security, calibration and maintenance, personnel training, emergency recovery and periodic re-evaluation

## Slide 45
System specification (Control document)
In place, stating:
  objectives of a proposed computer system
  the data to be entered and stored
  the flow of data
  how it interacts with other systems and procedures
  the information to be produced
  the limits of any variable
  the operating programme and test programme
System elements that need to be considered in computer validation include:
  hardware (equipment)
  software (procedures)
  people (users)

## Slide 46
Functional specification (Performance specification)
Provide instructions for:
  testing, operating, and maintaining the system
  names of the person(s) (development and operation)
When using computer systems, consideration:
  location
  power supply
  (Fluctuations in the electrical supply can influence computer systems and power supply failure can result in loss of memory).
  temperature
  magnetic disturbances

## Slide 47
Functional specification (Performance specification) (2)
GMP requirements for computer systems:
Verification and revalidation
  After a suitable period of running a new system
  Independently reviewed and compared with the system specification and functional specification
Change control
  Alterations made in accordance with a defined procedure
  Provision for checking, approving and implementing the change
Checks
  Data checked periodically
  Confirm accurate and reliable transfer

## Slide 48
Security
Production as well as in quality control
Data entered or amended - authorized persons
Security systems to prevent unauthorized entry or manipulation of data
SOPs for entering data, changing or amending incorrect entries and creating back-ups
Audit trail:
  identify the persons who made entries
  identify the persons who made changes
  identify the persons who released material
  identify the persons who performed other critical steps in production or control

## Slide 49
Independent verification and release for use by a second authorized person
  e.g. for entry of a master processing formula.
SOPs for certain systems or processes validated
  e.g. action in case of system failure or breakdown including disaster recovery procedure in the event of a breakdown
Back-ups
Regular back-ups of all files and data
  Secure storage (prevent intentional or accidental damage)

## Slide 50
Validation
Validation process should include:
  Planning
  Validation policy
  Project plan and SOPs
Define computer-related systems and vendors
Vendor and product evaluated
System designed and constructed
  Consider types, testing and quality assurance of the software
Extent of qualification depends on complexity of the system
Qualification includes:
Installation
Evaluation of the system
Performance
Change control, maintenance and calibration, security, contingency planning, SOPs, training, performance monitoring and periodic re-evaluation

## Slide 51
Validation of hardware
Appropriate tests and challenges to the hardware
No influence of static, dust, power-feed voltage fluctuations and electromagnetic interference
Hardware is considered to be equipment
  focus on location, maintenance and calibration as part of the Qualification
It should prove:
Appropriate capacity
Operational limits
  e.g. memory, connector ports, input ports
Performance under worst-case conditions
  e.g. long hours, temperature extremes
Reproducibility/consistency
  e.g. by performing at least three runs under different conditions

## Slide 52
Validation of hardware (2)
Written qualification protocols; results in qualification reports kept
Revalidation – in case of significant changes
Validation may be performed by the vendor – but ultimate responsibility remains with the company
If records kept by supplier, manufacturer still has to have sufficient records to allow assessment of the adequacy of the validation
A mere certification of suitability from the vendor, for example, will be inadequate

## Slide 53: Summary: Validation requirements for Hardware (See table 1 in notes)
Hardware types
Distribution
system
Peripheral
devices
Signal converter
Central
Processing
Unit
Input
devices
Output
devices

## Slide 54
Key aspects
To consider
Command
overrides
Maintenance
Signal
conversion
I/O operation
Location:
environment,
distances
Summary: Validation requirements for Hardware (See Table 1 in notes)

## Slide 55
Validation
Reproducibility
Consistency
and
documentation
Limits
Worst case
Revalidation
Function
Summary: Validation requirements for Hardware (See Table 1 in notes)

## Slide 56
Validation of Software
The term used to describe the complete set of programmes used by a computer, and which should be listed in a menu
Records are considered as software
Focus should be placed on:
  accuracy, security, access, retention of records, review, double checks, documentation and accuracy of reproduction

## Slide 57
Key computer programmes to be identified:
  language, name, function (purpose of the programme)
  input (determine inputs), output (determine outputs)
  fixed set point (process variable that cannot be changed by the operator), variable set point (entered by the operator)
  edits (reject input/output that does not conform to limits and minimize errors, e.g. four- or five-character number entry), input manipulation (and equations) and programme overrides (e.g. to stop a mixer before time)
Identification of authorized personnel
  to write, alter or have access to programmes

## Slide 58
Validation of Software (2)
Points to be considered may include:
  Consistency in performance: Within pre-established limits)
  Function: Matching the assigned operational function (e.g. generate batch documentation, different batches of material used in a batch listed)
  Worst case: Validation under different conditions (e.g. speed, data volume, frequency)
  Repeats: Sufficient number of times (e.g. replicate data entries)
  Documentation: Protocols and reports
  Revalidation: In case of significant changes made

## Slide 59
Level
High level
language
Assembly
language
Application
language
Machine
language
Summary: Validation requirements for Software (See Table 1 in notes)

## Slide 60
Software
identification
Fixed and
Variable
Set points
Edits,
input
manipulation
Name,
function
Input,
output
Programme
overrides
Language
Summary: Validation requirements for Software (See Table 1 in notes)

## Slide 61
Validation
Repeats
Worst case
Documentation
Revalidation
Function
Summary: Validation requirements for Software (See Table 1 in notes)

## Slide 62: Enterprise Resource Planning (ERP):-
It is an integrated computer-based system used to manage internal and external resources including tangible assets, financial resources, materials, and human resources.
It is a software architecture whose purpose is to facilitate the flow of information between all business functions inside the boundaries of the organization and manage the connections to outside stakeholders.

## Slide 63
Why ERP?
For Management – to know what is happening
in the company
One solution for better Management
For cycle time reduction
To achieve cost control & low working capital
To marry latest technologies
To shun the geographical gaps
To satisfy the customers with high expectations
To be Competitive & for survival

## Slide 64
Evolution of ERP
1960’s - Systems Just for Inventory Control
1970’s - MRP – Material Requirement Planning
(Inventory with material planning & procurement)
1980’s - MRP II – Manufacturing Resources Planning
(Extended MRP to shop floor & distribution Mgnt.)
Mid 1990’s - ERP – Enterprise Resource Planning
(Covering all the activities of an Enterprise)
2000 onwards – ERP II – Collaborative Commerce
(Extending ERP to external business entities)

## Slide 65
ERP Components –
Transactional backbone
Financials
Distributions
Human resources
Product lifecycle management
Advanced Applications
Customer relationship management (CRM)
Supply chain management
Purchasing
Manufacturing
Distribution
Warehouse management system
Management Portal/Dashboard

## Slide 66
Commercial Applications
1. Manufacturing
Engineering, bills of material, scheduling, capacity, workflow management, quality control, cost management, manufacturing process, manufacturing projects, manufacturing flow
2. Supply chain management
Order to cash, inventory, order entry, purchasing, product configurator, supply chain planning, supplier scheduling, inspection of goods, claim processing, commission calculation
3. Financials
General ledger, cash management, accounts payable, accounts receivable, fixed assets

## Slide 67
4. Project management
Costing, billing, time and expense, performance units, activity management
5. Human resources
Human resources, payroll, training, time and attendance, rostering, benefits
6. Customer relationship management
Sales and marketing, commissions, service, customer contact and call center support
7. Data services
8. Access control

## Slide 68: Advantages
ERP systems connect the necessary software in order for accurate forecasting to be done.
Integration among different functional areas to ensure proper communication, productivity and efficiency
Design engineering (how to best make the product)
Order tracking, from acceptance through fulfillment
The revenue cycle, from invoice through cash receipt
Managing inter-dependencies of complex processes bill of materials
Tracking the three-way match between purchase orders (what was ordered), inventory receipts (what arrived), and costing (what the vendor invoiced)
The accounting for all of these tasks: tracking the revenue, cost and profit at a granular level.

## Slide 69
ERP Systems centralize the data in one place. Benefits of this include:
Eliminates the problem of synchronizing changes between multiple systems - consolidation of finance, marketing and sales, human resource, and manufacturing applications
Permits control of business processes that cross functional boundaries
Provides top-down view of the enterprise (no "islands of information"), real time information is available to management anywhere, anytime to make proper decisions.
Reduces the risk of loss of sensitive data by consolidating multiple permissions and security models into a single structure.
Shorten production lead time and delivery time
Facilitating business learning, empowering, and building common visions

## Slide 70: Disadvantages
Customization of the ERP software is limited.
ERP systems can be very expensive
ERPs are often seen as too rigid and too difficult to adapt to the specific workflow and business process of some companies—this is cited as one of the main causes of their failure.
Many of the integrated links need high accuracy in other applications to work effectively.
Once a system is established, switching costs are very high for any one of the partners (reducing flexibility and strategic control at the corporate level).
The blurring of company boundaries can cause problems in accountability, lines of responsibility, and employee morale.
Resistance in sharing sensitive internal information between departments can reduce the effectiveness of the software.

## Slide 71: REFERENCES (1)
The United State Pharmacopoeia 24; The National Formulary 19; 2000: [1225] VALIDATION OF COMPENDIAL METHODS.
Paul a. winslow & richard F. meyer Compliance handbook of pharmaceutical, medical device, & biologics page no. 129-183, 218-256
www.fda.gov/ohrms/dockets/ ac/02/slides/ 3841s1_07_lachman.PPT
http://www.fda.gov/cder/guidance/ameth.htm
http://www.ich.org
WHO Technical Report Series,No. 937, 2006. Annex 4. Appendix 4
http://www.pharmtech.com/pharmtech/data/articlestandard/pharmtech/102003/48314/article.pdf
http://www.ivstandards.com/tech/reliability/part17.asp
http://www.aoac.org/

## Slide 72
www.fda.gov
www.computersystemvalidation.com
http://www.labcompliance.com/methods/meth_val.
http://www.fda.gov/cder/guidance/2396dft.htm
“Computers in Pharmaceutical Technology”, Encyclopedia of Pharmaceutical Technology, Volume 3
Schoushoe M. “Computer Validation Master Planning: Validation Strategies”, Pharmaceutical Technology, November 2005
Method Validation in Pharmaceutical Analysis Edited by
J. Ermer and J. H. McB. Miller
Facility validation Theory, Practice, and Tools by Graham C. Wrigley
Pharmaceutical process validation , Robert A. nash & Alfred H. wachter page no. 10-45, 265-278

## Slide 73
Therapeutics Products Programme. Process Validation: Aseptic Processes for Pharmaceuticals. http://www.hcsc.gc.ca/ hpbdgps/ therapeutic; downloaded March 30, 2001.
USP 25–NF 20 (United States Pharmacopeial Convention, Rockville MD, 2002), p. 2256.

## Slide 74
Thank you